Y2K

BENCHMARK REPORT FOR THE

ATSC ALPHA VMS COMPUTER

January 1999

Oscar Brogdon, Brion Conklin, Julie Horvath, Anthony Mann,

Dan Nugent, Jack Stevens, and Michele Veasey

Table of Contents

1.0	INTRODUCTION	1

1.1	General	1

1.2	Software Configuration	1

1.3	Year 2000 Algorithm	1

2.0	BENCHMARK DATA SET	1

3.0	ACQUISITION AND SCHEDULING	2

3.1	General	2

3.2	Acquisition	2

3.2.1	Description	2

3.2.2	Software Modifications	2

3.2.3	Test Procedures	2

3.2.4	Data Set	3

3.2.5	Results	3

3.3	Scheduling	3

3.3.1	Description	3

3.3.2	Software Modifications	3

3.3.3	Test Procedures	3

3.3.4	Data Set	3

3.3.5	Results	4

3.4	Timebias	4

3.4.1	Description	4

3.4.2	Software Modifications	4

3.4.3	Test Procedures	4

3.4.4	Data Set	4

3.4.5	Results	4

4.0	DATA FLOW AND POSTING	4

4.1	General	4

4.2	Data Posting	5

4.2.1	Description	5

4.2.2	Software Modifications	5

4.2.3	Test Procedures	5

4.2.4	Data Set	5

4.2.5	Results	5

4.3	Merit Tools	6

4.3.1	Description	6

4.3.2	Software Modifications	6

4.4	Quicklook Data Management	6

4.4.1	Description	6

4.4.2	Software Modifications	6

4.4.3	Test Procedures	6

4.4.4	Data Set	7

4.4.5	Results	7

5.0	DATABASES	7

5.1	General	7

5.2	Summary Database and Calibration Database	8

5.2.1	Description	8

5.2.2	Software Modifications	8

5.2.3	Test Procedures	8

5.2.4	Data Set	8

5.2.5	Results	9

5.3	SIDB and Target Database	9

5.3.1	Description	9

5.3.2	Test Procedures	9

5.3.3	Data Set	9

5.3.4	Results	9

5.4	CSTG Engineering Database (Sampled Quicklook Data)	9

5.4.1	Description	9

5.4.2	Software Modifications	9

5.4.3	Test Procedures	9

5.4.4	Data Set	10

5.4.5	Results	10

5.5	Normal Point Database	10

5.5.1	Description	10

5.5.2	Software Modifications	10

5.5.3	Test Procedures	10

5.5.4	Data Set	11

5.5.5	Results	11

5.6	TOR Database	11

5.6.1	Description	11

5.6.2	Software Modifications	11

5.6.3	Test Procedures	11

5.6.4	Data Set	12

5.6.5	Results	12

5.7	Quicklook Analysis Database	12

5.7.1	Description	12

5.7.2	Software Modifications	12

5.7.3	Test Procedures	12

5.7.4	Data Set	13

5.7.5	Results	13

6.0	PROCESSING AND DATA ANALYSIS	13

6.1	General	13

6.2	Crustal Dynamics Project Laser Processor	13

6.2.1	Description	13

6.2.2	Software Modifications	13

6.2.3	Test Procedures	14

6.2.4	Data Set	14

6.2.5	Results	14

6.3	Generic Normal Points	14

6.3.1	Description	14

6.3.2	Software Modifications	14

6.3.3	Test Procedures	14

6.3.4	Data Set	14

6.3.5	Results	15

6.4	GEODYN	15

6.4.1	Description	15

6.4.2	Software Modifications	15

6.4.3	Test Procedures	15

6.4.4	Data Set	15

6.4.5	Results	15

6.5	Polyquick	16

6.5.1	Description	16

6.5.2	Software Modifications	16

6.5.3	Test Procedures	16

6.5.4	Data Set	16

6.5.5	Results	16

6.6	Version “M” Headquarters	16

6.6.1	Description	16

6.6.2	Software Modifications	17

6.6.3	Test Procedures	17

6.6.4	Data Set	17

6.6.5	Results	17

7.0	CONCLUSION	17

APPENDICIES	A-1

Appendix A	LAGEOS GEODYN Vector Files	A-1

A.1	LAGEOS IV:	A-1

A.2	LAGEOS IV:	A-1

A.3	LAGEOS IV Difference (GEODYN 9310 vs. 9708)	A-2

A.4	LAGEOS IRV Difference (GEODYN 9310 vs. 9708)	A-2

Appendix B	Generic Normal Point Software	B-1

B.1	Introduction	B-1

B.2	Benchmark Test Set	B-1

B.3	Test Procedures	B-1

B.4	Results	B-1

B.5	Conclusions	B-1

Appendix C 	GEODYN and Generic Normal Point Analysis Results	C-1

List of Tables

Table 2.1 Year 2000 Benchmark Data Set	1

Table 3.1 Acquisition and Scheduling Software	2

Table 4.1 Data Flow and Posting Software	5

Table 4.2 Quicklook Files Copied to the CDDIS	7

Table 5.1 Databases	8

Table 5.2 TOR Database Data Set	12

Table 5.3 Quicklook Analysis Database Data Set	13

Table 6.1 Processing and Data Analysis Software	13

Table 6.2 Version “M” File Types	16

Table 7.1 Summary of Benchmark Tests	17

# 1.0	INTRODUCTION

## General

All operational NASA SLR software resident on the Alpha running VMS must be year 2000 compatible, and has been modified, as necessary to meet this requirement. This Benchmark Report describes the procedures used to verify the accuracy of the software, the results of the benchmark tests, and any discrepancies resulting from the test runs.

## Software Configuration

The Alpha VMS Software can be broken down into four functional software groups: 1) Acquisition and Scheduling, 2) Data Flow and Posting, 3) Databases, and 4) Processing and Analysis. The verification of the software in each of these groups is outlined in Sections 3-6.

## 1.3	Year 2000 Algorithm

The correct century must be determined for all 2-digit year fields. Therefore, all 2-digit year fields are converted to 4-digit year fields according to the following algorithm. If the year is less than or equal to 60, 2000 is added to the year. Otherwise, 1900 is added to the year. Henceforth, this conversion shall be referred to as the Year 2000 Algorithm.

# 2.0	BENCHMARK DATA SET

The Benchmark Data Set consists of Pre Year 2000 data, Post Year 2000 data, and data which crosses over from 1999 into 2000. Leap year was tested using February 29, 2000 and March 1, 2000 data. In addition, data crossing over from one year to the next was tested for non-leap year to non-leap year, leap year to non-leap year, and non-leap year to leap year. At least one pass for each type of satellite (low, medium, and high orbit) was tested. At least one pass from each of the following stations was tested: Moblas-4, Moblas-5, Moblas-6, Moblas-7, Moblas-8, Hollas, MLRS, TLRS-3, and TLRS-4. The benchmark data set is listed in Table 2.1.

| Start Time | End Time | Station | Satellite | Satid | Item Tested |
| --- | --- | --- | --- | --- | --- |
| May 31, 1998 | May 31, 1998 | Moblas 7 | Starlette | 1134 | Pre Year 2000 |
| Sep 5, 1998 | Sep 5, 1998 | TLRS-4 | Ajisai | 1500 | Pre Year 2000 |
| Sep 5, 1998 | Sep 5, 1998 | Moblas 4 | Ajisai | 1500 | Pre Year 2000 |
| Oct 24, 1998 | Oct 24, 1998 | TLRS-3 | Stella | 0643 | Pre Year 2000 |
| Nov 2, 1998 | Nov 2, 1998 | Hollas | Lageos | 1155 | Pre Year 2000 |
| Dec 31, 1999 | Jan 1, 2000 | Moblas 7 | GPS-36 | 3636 | Crossing Midnight – change in century |
| Jan 1, 2000 | Jan 1, 2000 | Moblas 7 | Lageos | 1155 | First Day of Century |
| Jan 15, 2000 | Jan 15, 2000 | Hollas | ERS-2 | 6178 | Year 2000 |
| Feb 29, 2000 | Feb 29, 2000 | Moblas 4 | Topex | 4377 | Leap Year |
| Mar 1, 2000 | Mar 1, 2000 | Moblas 5 | Starlette | 1134 | Leap Year |
| April 4, 2000 | April 4, 2000 | MLRS | Lageos 2 | 5986 | Year 2000 |
| Dec 31, 2000 | Jan 1, 2001 | Moblas 5 | GPS-35 | 3535 | Day 366 & Crossing Midnight- leap year to non leap year |
| Mar 1, 2001 | Mar 1, 2001 | TLRS-3 | GFZ-1 | 8001 | Non Leap Year |
| Dec 31, 2001 | Jan 1, 2002 | Moblas 8 | Etalon 1 | 0525 | Crossing Midnight – non leap year to non leap year |

Table 2.1 Year 2000 Benchmark Data Set

In addition to the benchmark data set listed above, other data was used to test particular software packages, in order to verify certain capabilities. This testing will be detailed in the specific sections below.

# 3.0	ACQUISITION AND SCHEDULING

## 3.1	General

The Acquisition and Scheduling Software can be subdivided into three groups: 1) Acquisition, 2) Scheduling, and 3) Time Bias.

| Software | Input | Output |
| --- | --- | --- |
| Acquisition | (Multiple) | .out and .tiv |
| Scheduling | SATELLITE.out | Schedule files |
| Timebias | (Multiple) | Timebias.lis |

Table 3.1 Acquisition and Scheduling Software

## 3.2	Acquisition

### 3.2.1	Description

The acquisition software package contains several programs, including: convert_ephem, iv_tuner, tuned_iv_to_irv and sight. Convert_ephem extracts from the GEODYN ephemeris, a vector once per hour, to perform the vector tuning process. Iv_tuner performs the fitting process, and tuned_iv_to_irv forms the tuned irv message files. Sight reads the complete GEODYN ephemeris and determines the time for each satellite pass for a designated set of stations.

### 3.2.2	Software Modifications

The year in the GEODYN ephemeris file is two digits, so the software had to be modified to determine what century the ephemeris was generated for. A check was added, so that if the year was less than 60, 100 years was added. This allows for the crossing of the century to be handled. At the end of the programs, the year is module 100, to convert the dates back to two digits. The tuned irv process uses modified Julian dates, so that the dates are contiguous. The year in the tuned irv format is four digits, so no modifications were necessary.

### 3.2.3	Test Procedures

Once the GEODYN upgrade was completed and verified, the acquisition software was verified. This procedure was as follows:

- Generate a GEODYN ephemeris file for each of the test cases.

- Execute the convert_ephem software.

- Modify the file that provides the dates to be tuned, and execute the iv_tuner software.

- Execute the tuned_iv_to_irv program.

- Modify the input file to Sight, and execute the software.

The output of each step was verified except for the conversion of the GEODYN ephemeris since this file is a binary format.

### 3.2.4	Data Set

The data set generated and tested is provided in Table 2.1.

### 3.2.5	Results

- GEODYN software was successfully executed generating an ephemeris file for each pass of the Y2K Benchmark Data Set.

- The convert_ephem software was successfully executed for each GEODYN ephemeris generating a file containing once-per-hour vectors.

- The iv_tuner software was successfully executed for each once-per-hour vector file.

- The tuned_iv_to_irv software was successfully executed generating the tuned irv message file.

- The sight software was successfully executed for each GEODYN ephemeris generating files which contain key pass information including times and durations for each satellite pass for all designated stations.

- These sight files were directly compared by hand to the Y2K Benchmark Data Set and were found to be identical.

- The acquisition software was found to be Y2K compliant.

## 3.3	Scheduling

### 3.3.1	Description

The scheduling software consists of two software packages. The first generates a summary of all of the passes available for any given station for a specified set of dates and times. The second provides a detailed sequence of events such as when calibrations should be taken and what satellites to track.

The first software package consists of three programs, shed, proc and glean. Shed reads the output from sight and a input file specifying what dates and output the extracted passes to an intermediate file. Proc extracts the passes that are within the specified times. Glean generates the schedule files for each station.

The second software package consists of two programs, formplan and SATCOP. Formplan updates the previous week’s schedule to the new one for input to SATCOP. SATCOP reads the scheduling information and the output of Sight, and then generates a schedule for each station.

### 3.3.2	Software Modifications

The modifications to both software packages required the handling of date changes from 991231 to 000101. To accomplish this, years less than 60 become the year plus 100. This is done so that the years are in time sequence. This modification also allowed for the conversion of the date to modified Julian date not to be changed since 1900 + 100 = 2000. For the output, the year is then module by 100.

### 3.3.3	Test Procedures

Output files for the dates specified in Table 3.1 were generated and schedules generated by the two packages. These schedules were checked against the output files via a visual inspection.

### 3.3.4	Data Set

The data set generated and tested is provided in Table 2.1.

### 3.3.5	Results

- The shed, proc, and glean software was successfully executed generating a 24-hour satellite available listing for each station.

- The formplan and SATCOP software was successfully executed generating a priority dependent satellite and calibration schedule for each station.

- All passes of the Y2K Benchmark Data Set were directly compared by hand to corresponding station schedules and were found to be identical.

- The scheduling software was found to be Y2K compliant.

## 3.4	Timebias

### 3.4.1	Description

The timebias software determines the range and time bias for each quicklook pass received each day. The information is stored in a simple database and then a satellite by satellite time bias average is determined for the past 5 days.

### 3.4.2	Software Modifications

The quicklook data contains only a two-digit year that has to be converted to a modified Julian date. To do this, the correct century must be determined. If the year is less than 60, then 2000 is added, else 1900 is added. The simple database was modified to support 4-digit years instead of 2-digit.

### 3.4.3	Test Procedures

The quicklook data generated by the field data processing computer for the Y2K tests was inputted into the timebias software and the results were visually verified.

### 3.4.4	Data Set

The data set generated and tested is provided in Table 2.1.

### 3.4.5	Results

- The timebias software was successfully executed generating a range and time bias for each pass of the Y2K Benchmark Data Set. This data was then merged with current data, and successfully sorted by date and time.

- The timebias software also generated a list of daily averaged time biases for each satellite for the Y2K Benchmark Data Set. (There is no way to verify the accuracy of the time bias information because all data was simulated.)

- The timebias software was found to be Y2K compliant.

# 4.0	DATA FLOW AND POSTING

## 4.1	General

The Data Flow and Posting Software includes 1) Data Posting, 2) Merit Tools, and 3) Quicklook Data Management.

| Software | Input | Output |
| --- | --- | --- |
| Data Posting | Merit II Full-rate | Merit II Full-rate |
| Merit Tools | Merit II Full-rate | Summary Listing |
| Quicklook Data Management | CSTG and Engineering Quicklook | Quicklook data on the CDDIS |

Table 4.1 Data Flow and Posting Software

## 4.2	Data Posting

### 4.2.1	Description

The Data Posting Software accepts Merit II Full-rate data, which has been transferred from the sites to headquarters and deposited into a holding directory. The Data Posting Software sorts the data by date and time and separates it into files based on station / satellite combinations. The sorted and separated data is copied to the CDDIS.

### 4.2.2	Software Modifications

Since the Merit II format contains only a 2-digit year field, a simple numeric sort on the time field, which is performed by the old Data Posting Software, will not produce the desired results for year 2000 data. Therefore, additional software was written to perform the sort function, taking into account the 4-digit year field, and added to the Data Posting Software Package.

### 4.2.3	Test Procedures

The accuracy of the new sorting software was verified. In addition, the final product, Merit II data separated by station and satellite, was verified.

The Merit II Full-rate data, which is deposited in the holding directory (the input to DataPost), was compared with the Merit II full-rate data deposited on the CDDIS (the output from DataPost). All data in the original holding directory should be present on the CDDIS. The files in the holding directory are separated by station, only. The files on the CDDIS are separated by station / satellite combinations. Therefore, the files in the holding directory were examined to determine what satellites were present. The files on the CDDIS must represent all satellites for the given station, for the given day.

The data on the CDDIS was examined to verify it is sorted correctly by time.

### 4.2.4	Data Set

The data set generated and tested is described in section 2.1.

### 4.2.5	Results

- All test data sets were successfully written to the proper satellite and station file combinations with appropriate file naming conventions. These files, located on the VAX Alpha, were subsequently transferred to the CDDIS Unix computer facility for inspection by the CDDIS manager and staff. No problems or concerns were reported.

## 4.3	Merit Tools

### 4.3.1	Description

The Merit Tools Software was used to sort, merge, copy, and summarize Merit II full-rate data. This software is now obsolete, but has been archived.

### 4.3.2	Software Modifications

Since the Merit Tools Software is obsolete, no changes were made to the software for year 2000 compatibility.

## 4.4	Quicklook Data Management

### 4.4.1	Description

The Quicklook Data Management Software accepts CSTG format data in .QLD files. The input data is taken from three sources:

- The LTNCOM account, containing NASA station data.

- The CDDIS, for foreign station data.

- The FG_NORMPTS account, for stations such as Orroral.

The quicklook data is filtered, sorted by satellite, and then distributed. The quicklook data:

- Is copied to the CDDIS in files sorted by satellite, and as larger files.

- Is loaded into the Quicklook Analysis Database (Oracle)

- Is loaded into the Normal Point Database (binary).

- Is loaded into the CSTG Engineering Database (binary).

The software to manipulate the databases (E, F, and G, above) is detailed separately under Section 5.

### 4.4.2	Software Modifications

The CSTG format, which contains a 2-digit year field, was not modified for year 2000 compatibility. The software to handle the distribution of the CSTG format data to the CDDIS required no modifications for year 2000.

### 4.4.3	Test Procedures

Even though no software modifications were made, the software to handle the collection and distribution of the CSTG format data to the CDDIS was tested to verify the flow of the data.

Table 4.2 gives an example of a daily file, SEP08.DAT, which is broken down into separate files, which are sent to the CDDIS.

| Quicklook File | Files Copied to CDDIS | Description |
| --- | --- | --- |
| SEP08.DAT | ALL_QL980908.ALL | All data for 9/8/1998 |
|  | NASA_QL980908.DAT | NASA stations only for 9/8/1998 |
|  | NEW_QL980908.TOP | Topex data only for 9/8/1998 |
|  | NEW_QL980908.LAG | Lageos data only for 9/8/1998 |

Table 4.2 Quicklook Files Copied to the CDDIS

Preliminary tests were run on current data. Eight daily input files of CSTG normal points (e.g. SEP08.DAT) were compared by hand with the final daily files sent to the CDDIS (ALL_QL980908.dat and NASA_QL980908.dat), and with the satellite specific files sent to the CDDIS (e.g. NEW_QL980908.TOP). All fields should match. These final daily files and satellite specific files, which are stored on the quicklook account, were verified to ensure they were copied completely to the appropriate directories on the CDDIS.

The Year 2000 Benchmark Data Set (Table 2.1) was run through all of the software used in Quicklook Data Management (QLDM), except the last function, and delivered to the CDDIS. Since the QLDM System copies data to the CDDIS, and the simulated data should not be copied to the CDDIS, the complete process could not be run on the Year 2000 Benchmark Data Set. The files to be copied to the CDDIS, were created and hand checked, but not sent to the CDDIS.

### 4.4.4	Data Set

Quicklook data from the Year 2000 Benchmark Data Set (Table 2.1) was merged into one file and processed through the Quicklook Data Management System.

In addition, daily quicklook files for the following dates were run through the Quicklook Data Management Software.

Sep 1, 1998			Sep 8, 1998

Sep 2, 1998			Sep 10, 1998

Sep 3, 1998			Sep 11, 1998

Sep 7, 1998			Sep 12, 1998

### 4.4.5	Results

- The input daily quicklook files (e.g. SEP08.DAT) all matched with the corresponding merged files sent to the CDDIS (e.g. NEWQL980908.DAT), and with the daily satellite specific files sent to the CDDIS (e.g. NEWQL980908.TOP and NEWQL980908.LAG). In addition, the merged files and the satellite specific files were compared before and after transmission to the CDDIS; and were identical.

- The simulated year 2000 daily file also matched the file output from the Quicklook Data Management System. This file was hand-checked, but not sent to the CDDIS.

- The Quicklook Data Management System successfully passed Year 2000 Benchmark Testing.

# 5.0	DATABASES

## 5.1	General

The software included in the Databases category is listed in Table 5.1.

| Software | Input | File Format |
| --- | --- | --- |
| Calibration Database | Version M Processing Statistics | Binary VMS Indexed File (old), Oracle (new) |
| CSTG Engineering Database | Sampled Engineering Quicklook | Binary VMS Indexed File |
| Normal Point Database | CSTG Normal Points | Binary VMS Indexed File |
| Quicklook Analysis Database | Quicklook Processing Statistics | Oracle |
| SIDB | Station Geodetic Information | Binary VMS Indexed File |
| Summary Database | Version M Processing Statistics | Binary VMS Indexed File (old), Oracle (new) |
| Target Database | Target Information | Binary VMS Indexed File |
| TOR Database | Laser Operations Reports (LORs) | Oracle |

Table 5.1 Databases

## 5.2	Summary Database and Calibration Database

### 5.2.1	Description

The Summary Database and Calibration Database are maintained at headquarters and contain processing statistics from the on-site HPLDP and the Generic Normal Point software packages. Currently, these databases are VMS Indexed files resident on the VAX Open VMS machine, and contain 2-digit year fields. These databases and their corresponding software are not year 2000 compliant. In addition, some of the fields in both databases are not used and user access to the databases could be simplified. Therefore, a complete redesign of both databases was performed at the same time as the modificaitons for Year 2000 compliance.

### 5.2.2	Software Modifications

The Summary Database and the Calibration Database were redesigned from VMS indexed files on the VAX Open VMS to Oracle databases on the Alpha Windows NT platform. The Oracle databases are loaded on a daily basis using the SQL*Loader. A newly written VMS command procedure is used to automatically transfer the input data (Version M on-site processing statistics) from the VAX Open VMS to an Oracle load file.

### 5.2.3	Test Procedures

Since the Summary Database and the Calibration Database were completely redesigned, all fields were checked for accuracy. The input data file for each database was hand-checked with the loaded fields to verify the numbers were correct. In addition, the automatic procedures which load the databases were tested to verify they run correctly.

The new Oracle Databases have been run in parallel with the operational VMS Indexed File Databases since July 31, 1998.

### 5.2.4	Data Set

The data set generated and tested is described in section 2.1.

### 5.2.5	Results

## 5.3	SIDB and Target Database

### 5.3.1	Description

The Station Information Database (SIDB) and the Target Database contain four-digit date fields. The input data, geodetic information and target information, respectively, also contain 4-digit date fields. Therefore, no changes were necessary to any of the SIDB or Target Database software for year 2000 compatibility.

### 5.3.2	Test Procedures

The SIDB and Target Database Software are currently operational, running on 1998 data. These databases contain one line of geodetic or target information for each time period. A line of data was added to cover each of the time spans listed in Table 2.1.

### 5.3.3	Data Set

The data set generated and tested is provided in Table 2.1.

### 5.3.4	Results

- The Target Database was temporally updated to incorporate Y2K conditions described in Table 2.1. Each file was processed utilizing the CDPLP processor V8_2 to examine results produced from the updated Target Database.

- Results from the CDPLP were found to be Y2K compliant.

## 5.4	CSTG Engineering Database (Sampled Quicklook Data)

### 5.4.1	Description

The CSTG Engineering Database contains sampled quicklook data, which has been processed through the Quicklook Data Management System. The format of the database was changed for year 2000 compatibility. The date field was changed from 2 digits to 4 digits.

### 5.4.2	Software Modifications

Since the format of the CSTG Engineering Database was changed for year 2000 compatibility, the corresponding software to manipulate the database was modified, and must be verified for accuracy.

### 5.4.3	Test Procedures

The routines to update, delete, and extract records from the database were verified.

To verify the update routine, at least eight sample engineering quicklook format passes must be selected and captured prior to being used as input to the Quicklook Database Management System. Database extracts for the selected data were run. The results were compared by hand with the input passes, to verify the dates were loaded properly. In addition the passes generated by the field software were loaded into the database and extracted and passed through GEODYN.

In order to verify the delete routine, a snapshot of the database must be made before and after a delete command to verify the designated pass(es) were deleted with no side effects. At least four separate delete commands was done.

At least four separate database extracts were performed on the database to verify the desired selection criteria are being met.

### 5.4.4	Data Set

The data set generated and tested is provided in Table 2.1. In addition, the database has been updated in parallel with the present operational database.

### 5.4.5	Results

- The date field of the CSTG Engineering Database was changed from 2 digits to 4 digits to accommodate the year 2000.

- The update routine was successfully executed updating the CSTG Engineering Database with the passes of the Y2K Benchmark Data Set.

- The extract software was successfully executed generating a GEODYN Tracking Data Format file for each pass of the Y2K Benchmark Data Set.

- Each Tracking Data Format file was successfully used as an input to GEODYN.

- Four passes were successfully deleted from the database verifying the delete routine.

- The CSTG Engineering Database, the update routine, the extract software and the delete routine were found to be Y2K compliant.

- No anomalies have been observed with the daily updates.

## 5.5	Normal Point Database

### 5.5.1	Description

The Normal Point Database contains CSTG Normal Points, which have been processed through the Quicklook Database Management System. The format of the database was changed for year 2000 compatibility. The date field was changed from 2 digits to 4 digits.

### 5.5.2	Software Modifications

Since the format of the database was changed for year 2000 compatibility, the corresponding software to manipulate the database was modified, and must be checked for accuracy.

### 5.5.3	Test Procedures

The routines to update, delete, and extract records from the database were verified.

To verify the update routine, at least eight CSTG Normal Point Format passes must be selected and captured prior to being used as input to the Quicklook Database Management System. Database extracts for the selected data were run. The results were compared by hand with the input passes to verify the passes were loaded properly. In addition the passes generated by the field software were loaded into the database and extracted and passed through GEODYN.

In order to verify the delete routine, a snapshot of the database must be made before and after a delete command to verify the designated passes were deleted with no side effects. At least four separate delete commands were done.

At least four separate database extracts were performed on the database to verify the desired selection criteria are being met.

### 5.5.4	Data Set

See Table 2.1 in addition the database has been updated in parallel with the present operational database.

### 5.5.5	Results

- The date field of the Normal Point Database was changed from 2 digits to 4 digits to accommodate the year 2000.

- The update routine was successfully executed updating the Normal Point Database with the passes of the Y2K Benchmark Data Set.

- The extract software was successfully executed generating a GEODYN Tracking Data Format file for each pass of the Y2K Benchmark Data Set.

- Each Tracking Data Format file was successfully used as an input to GEODYN.

- Four passes were successfully deleted from the database verifying the delete routine.

- The Normal Point Database, the update routine, the extract software and the delete routine were found to be Y2K compliant.

- No anomalies have been observed with the daily updates.

## 5.6	TOR Database

### 5.6.1	Description

The Tracking Operations Report (TOR) Database is an Oracle Database containing information from the daily Laser Operations Reports (LORs). The LORs are automatically deposited in a holding directory on the VAX Alpha resident at headquarters. The LORs are hand edited, as necessary, reformatted, copied to a PC, and loaded into Oracle. The TOR Database consists of three tables in Oracle: Passes_DB, containing general pass information, Remarks_DB, containing the operator remarks contained in the LOR, and Timing_DB, containing timing information.

### 5.6.2	Software Modifications

The input LORs have a 2-digit year field. Since the format of the LORs was not changed for year 2000 compatibility, the software, which reads the 2-digit year in the LORs, was modified to  output a 4-digit year. This 4-digit year field is in the load file for Oracle. The software was modified according to the Year 2000 Algorithm (Section 1.3).

### 5.6.3	Test Procedures

Current daily LOR files were compared, by hand, with the values in the TOR Databases in Oracle. All fields should match. The extract from the TOR Database was done using Microsoft Query.

The data after 1999, inclusive, from the Benchmark Data Set (nine passes from Table 2.1) was loaded into the TOR Database. The newly loaded data was extracted from the database using Microsoft Query. The date fields were checked by hand to verify the correct date was loaded. Other fields were spot-checked.

In addition, the SQL*Load files were checked to verify they contained 4-digit year fields, and were formatted properly.

### 5.6.4	Data Set

The nine passes after December 1, 1999 from the Year 2000 Benchmark Data Set (listed in Table 3.1) were used to test the TOR Database Software. In addition, the following current files were used.

| File | Dates | Stations |
| --- | --- | --- |
| 267W001.LOR | 9/22/1998 – 9/23/1998 | Moblas 4, Moblas 5, Moblas 7, Moblas 8 MLRS, TLRS-3 |
| 268W001.LOR | 9/23/1998 – 9/24/1998 | Moblas 5, Moblas 7, Moblas 8, MLRS, TLRS-3 |

Table 5.2 TOR Database Data Set

### 5.6.5	Results

- The hand comparisons of the daily LORs and the extract from the TOR Database were done with no differences uncovered. The date fields from the Year 2000 Data Set were identical.

- The load files for Oracle contained accurate 4-digit date fields. The format of the load files was verified to be correct.

- The TOR Database Software successfully passed Year 2000 Benchmark Testing.

## 5.7	Quicklook Analysis Database

### 5.7.1	Description

The Quicklook Analysis Database is an Oracle Database containing information from the CSTG Normal Points and the Sampled Engineering Quicklook, which are received at headquarters from the stations on an hourly basis. The database is loaded daily. This software was modified according to the Year 2000 Algorithm (Secrion 1.3).

### 5.7.2	Software Modifications

The CSTG Format has a 2-digit year field. Since this format was not changed for year 2000 compatibility, the software, which reads the 2-digit year was modified to output a 4-digit year. This 4-digit year field is in the load file for Oracle.

### 5.7.3	Test Procedures

Current quicklook data files (.QLD files) were compared by hand with the values in the Quicklook Analysis Database in Oracle. All fields should match. The extract from the Quicklook Analysis Database was done using Microsoft Query.

The data after 1999, inclusive, from the Benchmark Data Set (nine passes from Table 2.1) was loaded into the Quicklook Analysis Database. The newly loaded data was extracted from the database using Microsoft Query. The date fields were checked by hand to verify the correct date was loaded. Other fields were spot-checked.

In addition, the SQL*Load file (.CTL) for all files described above were checked to verify they contained 4-digit year fields, and were formatted properly.

### 5.7.4	Data Set

The nine passes after December 1, 1999 from the Year 2000 Benchmark Data Set, listed in Table 2.1, were used to test the Quicklook Analysis Database Software. In addition, the following current data was used.

| Date | Time | Station | Satellite |
| --- | --- | --- | --- |
| 9/29/1998 | 15:00 | Moblas 4 | 1155 |
| 9/29/1998 | 12:32 | Moblas 4 | 3636 |
| 9/29/1998 | 08:20 | Moblas 4 | 5986 |
| 9/29/1998 | 23:38 | Moblas 7 | 4377 |
| 9/29/1998 | 19:48 | Moblas 7 | 1134 |

Table 5.3 Quicklook Analysis Database Data Set

### 5.7.5	Results

- The hand comparisons of the input quicklook files and the extract from the Quicklook Analysis Database were done with no differences uncovered. The date fields from the Year 2000 Data Set were identical.

- The load files for Oracle contained the accurate 4 digit date fields. The format of the load files was verified to be correct.

- The Quicklook Analysis Database Software successfully passed Year 2000 Benchmark Testing.

# 6.0	PROCESSING AND DATA ANALYSIS

## 6.1	General

The Processing and Data Analysis Software is listed in Table 6.1.

| Software | Input | Output |
| --- | --- | --- |
| CDPLP | LMT 88-byte | (Multiple) |
| Generic Normal Points | Merit II Full-rate | (Multiple) |
| GEODYN – G2E | (Multiple) | Interface, obs. file |
| GEODYN – G2S | Interface, sat obs | (Multiple) |
| Polyquick | Merit II Full-rate |  |
| Version “M” | .zip file | (Multiple) |

Table 6.1 Processing and Data Analysis Software

## 6.2	Crustal Dynamics Project Laser Processor

### 6.2.1	Description

The Crustal Dynamics Project Laser Processor (CDPLP) accepts LMT 88-byte data received from the sites and produces six output format types. The CDPLP processing software generates station/satellite tracking statistics utilized for performance analysis.

### 6.2.2	Software Modifications

Numerous routines in the CDPLP required modifications for Year 2000 compatibility. Routines were changed for:

- Modified Julian Day computations

- Date manipulations from one format to another

- Output year formats

To determine the correct century, given a 2-digit year field, the Year 2000 Algorithm (Section 1.3) was used.

In addition to the Year 2000 software modifications, the CDPLP was modified extensively, to redesign the output graphics capabilities. The new output graphics files are in a format used for creating IDL graphics.

The new version of the CDPLP is 8.2.

### 6.2.3	Test Procedures

The CDPLP processor was verified by running each data set from the benchmark data set through the CDPLP processor version 8.2.  All output files generated from the CDPLP processor was hand checked for accuracy and Y2k compliance.

### 6.2.4	Data Set

The Year 2000 benchmark data set, described in Table 2.1, was used for testing of the CDPLP. In addition, problem data from previous benchmarks of the CDPLP will be included in the CDPLP benchmark data set, to verify the software handles problem data.

### 6.2.5	Results

Each data set described in Table 2.1 was processed utilizing the CDPLP V8_2 processor.

- All test files were successfully processed and found to be Y2K compliant.

- All expected output files were produced with associated results identified as accurate and Y2k compliant.

## 6.3	Generic Normal Points

### 6.3.1	Description

The Generic Normal Point software was extensively rewritten with new algorithms to improve the normal point generation. The Y2K modifications were included in this rewrite of the software. This software now allows for the creation of CSTG format normal points on the VAX. Only Merit II normal points were created before.

### 6.3.2	Software Modifications

An extensive rewrite, mostly not related to Y2K, was done on the Generic Normal Point software.

### 6.3.3	Test Procedures

The Y2K data set was processed by the new generic normal point software. The redulting Merit II normal points were visually compared to the normal point data generated by the field normal point software.

### 6.3.4	Data Set

The data set generated and tested is provided in Table 2.1.

### 6.3.5	Results

- The results for the non-Y2K verification are shown in the benchmark report (Appendix A) for the new software. The Y2K tests found the Generic Normal Point software to be compliant.

## 6.4	GEODYN

### 6.4.1	Description

GEODYN is the basis for all of the orbit determination performed on the VAX. The version of the software is 9310. This software is maintained by GSFC, and ATSC ports the UNIX version of the software to the VAX.

### 6.4.2	Software Modifications

The version of GEODYN that was being used was version 9310, and was found to be non-compliant. The most recent operational version maintained by GSFC is version 9708, which is Year 2000 compliant.

### 6.4.3	Test Procedures

The software was compared against the previous version 9310, using all of the operational satellites. The punch files were compared visually, and the ephemeris files were compare via software that is used routinely for this purpose. Once this benchmark was completed, a test was performed checking the GEODYN ephemeris crossing from 12/31/1999 to 1/1/2000. The dates, times, vectors and Greenwich hour angles were visually checked for discontinuities. For the rest of the test data set, a check was performed to be sure that the dates agreed.

### 6.4.4	Data Set

The initial data set included present day 1998 quicklook data. The Y2K data set is presented in Table 2.1.

### 6.4.5	Results

- The GEODYN software was successfully executed generating ephemerides using the Y2K Benchmark Data Set that contain continuous data that starts in the year 1999 and ends in the year 2001

- The software was compared against the previous version 9310, using all of the operational satellites. The punch GEODYN files were compared visually, and the ephemeris files were compare via software that is used routinely for this purpose. Once this benchmark was completed, a test was performed checking the GEODYN ephemeris crossing from 12/31/1999 to 1/1/2000. The dates, times, vectors and Greenwich hour angles were visually checked for discontinuities. For the rest of the test data set, a check was performed to be sure that the dates agreed.   Sample Lageos iv, irv, iv difference and irv difference files are available in Appendix A.

- A very minor discrepancy was found in the inertial vector, and was traced back to the Greenwich hour angle. This difference was on the order of about 1.0 e –12. This was about 2.5 millimeters at the range of LAGEOS. The IRVs were compared with no differences. Since the vectors used to track are the IRVs, and the IRVs are used to determine the predicted ranges, this difference has no impact in the orbit determination performed on the VAX. The Y2K aspects of the test found no errors (see Appendix A).

- The GEODYN software was found to be Y2K compliant.

## 6.5	Polyquick

### 6.5.1	Description

Polyquick is the primary software package utilized to analyze and inter-compare simultaneous satellite tracking by 2 or more stations. Polyquick is also used to compare a single station’s data against itself to verify performance capabilities.

### 6.5.2	Software Modifications

### 6.5.3	Test Procedures

Polyquick was tested by comparing all data sets described in Table 2.1 against 8 other test files. Duplicate files were generated, with fictitious Sight Occupancy Designators (SOD) applied in order to fulfill the requirement for a 2 station comparison.

### 6.5.4	Data Set

The data set presented in Table 2.1 was utilized in conjunction with a duplicate data set generated with fictitious Site Occupancy Designators.

### 6.5.5	Results

- All polyquick output files returned the desired results of 0.0 bias between the compared data files.

- Additionally, all files outputs returned values which were Y2K compliant.

## 6.6	Version “M” Headquarters

### 6.6.1	Description

The Version “M” Headquarters Software accepts data from the field stations in eight different formats, as indicated in Table 6.2.

| File Type | Description | Status |
| --- | --- | --- |
| .fx | Raw LMT 88-byte | Saved (ground tests only). |
| .sm | Processor and Generic Normal Point summary | Saved. |
| .mrt | Merit II full-rate | Deposited in holding directory, for further processing by Data Posting Software (Section 5.2). |
| .npt | Merit II normal points | Deleted. |
| .pcr | Summary Database (Pass) capture record | Deposited in holding directory, for further processing by Summary Database Software (Section 6.2). |
| .ccr | Calibration Database capture record | Deposited in holding directory, for further processing by Calibration Database Software (Section 6.2). |
| .sdb | Generic Normal Point summary record | Deleted. |
| .qld | CSTG normal point and Sampled Engineering | Deposited in holding directory, for further processing by Quicklook Data Management System (Section 5.4). |

Table 6.2 Version “M” File Types

The data is separated, by file type, and distributed to the appropriate locations for further handling.

### 6.6.2	Software Modifications

Table 6.2 files have a 2-digit year field in the file name (e.g. S87Y98D357T1018_1134.sm.) However, the date in the file name is not used by the software, and does not impact the data flow. Therefore, no software modifications were necessary to the Version “M” Headquarters Software for Year 2000 compliance.

### 6.6.3	Test Procedures

Each file type processed by the Version “M” Headquarters Software was checked, by hand, to verify it was deposited completely in the appropriate directory.

### 6.6.4	Data Set

The Year 2000 Benchmark Data Set, listed in Table 2.1, was used to verify the Version “M” Headquarters Software.

### 6.6.5	Results

- The operations, file transfer and deletion, on the file types in Table 6.2 were successful.

# 7.0	CONCLUSION

All operational software resident on the VAX Alpha running Open VMS was benchmark tested, as outlined in this report. The results are summarized in Table 7.1. Additional results the Generic Normal Points and GEODYN may be found in Appendix B and Appendix C, respectively.

| Category | Software Package | Test Results | Comments |
| --- | --- | --- | --- |
| Acquisition & Scheduling | Acquisition Scheduling Timebias | Passed Passed Passed |  |
| Data Flow & Posting | Data Posting Merit Tools QL Data Management | Passed Not Tested Passed | Obsolete |
| Databases | Calibration CSTG Engineering Normal Point Quicklook Analysis SIDB Summary Target TOR | Passed Passed Passed Passed Passed Passed Passed Passed |  |
| Processing & Data Analysis | CDPLP Generic Normal Points GEODYN Polyquick Version “M” Headquarters | Passed Passed Passed Passed Passed | See Appendix A See Appendix B |

Table 7.1 Summary of Benchmark Tests

Based on these test results, all operational VAX Alpha Open VMS software has been modified successfully for year 2000 compliance, while retaining its previous functionality, and is ready for operational implementation.

# APPENDICIES

## Appendix A	LAGEOS GEODYN Vector Files

### A.1	LAGEOS IV:

19990365 85200.0      666209.85637    -9899619.73318    -7135952.65524 -2591.6180512  2863.6200121 -4222.4491866

19990365 85320.0      354331.87691    -9540612.24997    -7631159.82608 -2604.9864112  3118.2597308 -4028.8485149

19990365 85440.0       41340.63105    -9151632.11223    -8102371.77380 -2610.1683403  3363.0327310 -3822.6361255

19990365 85560.0     -271780.55050    -8733909.99555    -8548114.52107 -2607.1523070  3597.1669476 -3604.4756775

19990365 85680.0     -584048.55450    -8288767.10098    -8966996.02538 -2595.9534506  3819.9260959 -3375.0686813

19990365 85800.0     -894483.67764    -7817610.71782    -9357710.57097 -2576.6134308  4030.6120365 -3135.1519764

19990365 85920.0    -1202112.79515    -7321929.51252    -9719042.85167 -2549.2001811  4228.5669768 -2885.4951030

19990365 86040.0    -1505972.49420    -6803288.56318   -10049871.73250 -2513.8075697  4413.1755064 -2626.8975807

19990365 86160.0    -1805112.16124    -6263324.16019   -10349173.67997 -2470.5549712  4583.8664603 -2360.1861083

19990365 86280.0    -2098597.01280    -5703738.39377   -10616025.85210 -2419.5867534  4740.1146062 -2086.2116969

20000001     0.0    -2385511.05981    -5126293.54959   -10849608.84123 -2361.0716825  4881.4421563 -1805.8467494

20000001   120.0    -2664959.99585    -4532806.33369   -11049209.06365 -2295.2022521  5007.4200986 -1519.9820993

20000001   240.0    -2936074.00051    -3925141.94842   -11214220.79197 -2222.1939389  5117.6693511 -1229.5240182

20000001   360.0    -3198010.44931    -3305208.04056   -11344147.82729 -2142.2843907  5211.8617364  -935.3912064

20000001   480.0    -3449956.52229    -2674948.54309   -11438604.80955 -2055.7325508  5289.7207799  -638.5117742

20000001   600.0    -3691131.70389    -2036337.43179   -11497318.16564 -1962.8177221  5351.0223321  -339.8202252

20000001   720.0    -3920790.16724    -1391372.41758   -11520126.69611 -1863.8385770  5395.5950177   -40.2544507

20000001   840.0    -4138223.03644     -742068.59522   -11506981.80226 -1759.1121148  5423.3205129   259.2472573

20000001   960.0    -4342760.52095      -90452.06896   -11457947.35642 -1648.9725734  5434.1336545   557.7491639

20000001  1080.0    -4533773.91659      561446.42495   -11373199.21935 -1533.7702961  5428.0223820   854.3210137

### A.2	LAGEOS IV:

19990365 85200.0    -9920176.96343      190775.91156    -7135952.65524  3090.5430278  3058.1590422 -4222.4491866

19990365 85320.0    -9531107.03114      553924.13224    -7631159.82608  3392.0943547  2991.8856166 -4028.8485149

19990365 85440.0    -9106544.50191      908254.70002    -8102371.77380  3681.8927175  2911.2709696 -3822.6361255

19990365 85560.0    -8647968.47529     1252074.17051    -8548114.52107  3958.8004772  2816.7841326 -3604.4756775

19990365 85680.0    -8156991.56145     1583749.17040    -8966996.02538  4221.7308616  2708.9568229 -3375.0686813

19990365 85800.0    -7635353.50660     1901713.75717    -9357710.57097  4469.6524307  2588.3806871 -3135.1519764

19990365 85920.0    -7084914.29875     2204476.43171    -9719042.85167  4701.5932706  2455.7042770 -2885.4951030

19990365 86040.0    -6507646.78707     2490626.77289   -10049871.73250  4916.6449022  2311.6297750 -2626.8975807

19990365 86160.0    -5905628.85021     2758841.66523   -10349173.67997  5113.9658893  2156.9094906 -2360.1861083

19990365 86280.0    -5281035.15021     3007891.09327   -10616025.85210  5292.7851338  1992.3421463 -2086.2116969

20000001     0.0    -4636128.51026     3236643.47888   -10849608.84123  5452.4048500  1818.7689767 -1805.8467494

20000001   120.0    -3973250.95527     3444070.54003   -11049209.06365  5592.2032073  1637.0696581 -1519.9820993

20000001   240.0    -3294814.45546     3629251.65232   -11214220.79197  5711.6366373  1448.1580944 -1229.5240182

20000001   360.0    -2603291.41353     3791377.69702   -11344147.82729  5810.2417997  1252.9780772  -935.3912064

20000001   480.0    -1901204.93651     3929754.38205   -11438604.80955  5887.6372043  1052.4988442  -638.5117742

20000001   600.0    -1191118.93358     4043805.02468   -11497318.16564  5943.5244888   847.7105547  -339.8202252

20000001   720.0     -475628.08147     4133072.78765   -11520126.69611  5977.6893504   639.6197055   -40.2544507

20000001   840.0      242652.30141     4197222.36247   -11506981.80226  5990.0021329   429.2445061   259.2472573

20000001   960.0      961096.43071     4236041.09635   -11457947.35642  5980.4180724   217.6102345   557.7491639

20000001  1080.0     1677078.24087     4249439.56173   -11373199.21935  5948.9772023     5.7445933   854.3210137

### A.3	LAGEOS IV Difference (GEODYN 9310 vs. 9708)

date 19980109 seconds     0    radial  0.000    cross  -0.048    along  0.019    timebias 0.0000

date 19980109 seconds   240    radial  0.000    cross  -0.045    along  0.019    timebias 0.0000

date 19980109 seconds   480    radial  0.000    cross  -0.042    along  0.019    timebias 0.0000

date 19980109 seconds   720    radial  0.000    cross  -0.038    along  0.019    timebias 0.0000

date 19980109 seconds   960    radial  0.000    cross  -0.034    along  0.019    timebias 0.0000

date 19980109 seconds  1200    radial  0.000    cross  -0.029    along  0.019    timebias 0.0000

date 19980109 seconds  1440    radial  0.000    cross  -0.024    along  0.019    timebias 0.0000

date 19980109 seconds  1680    radial  0.000    cross  -0.019    along  0.019    timebias 0.0000

date 19980109 seconds  1920    radial  0.000    cross  -0.013    along  0.019    timebias 0.0000

date 19980109 seconds  2160    radial  0.000    cross  -0.007    along  0.019    timebias 0.0000

date 19980109 seconds  2400    radial  0.000    cross  -0.002    along  0.019    timebias 0.0000

date 19980109 seconds  2640    radial  0.000    cross   0.004    along  0.019    timebias 0.0000

date 19980109 seconds  2880    radial  0.000    cross   0.010    along  0.019    timebias 0.0000

date 19980109 seconds  3120    radial  0.000    cross   0.016    along  0.019    timebias 0.0000

date 19980109 seconds  3360    radial  0.000    cross   0.021    along  0.019    timebias 0.0000

date 19980109 seconds  3600    radial  0.000    cross   0.026    along  0.019    timebias 0.0000

Note: For the Difference files, all radial track, cross track and along track differences are in units of meters.  The timebias unit is seconds.

### A.4	LAGEOS IRV Difference (GEODYN 9310 vs. 9708)

date 19980109 seconds     0    radial  0.000    cross   0.000    along  0.000    timebias 0.0000

date 19980109 seconds   240    radial  0.000    cross   0.000    along  0.000    timebias 0.0000

date 19980109 seconds   480    radial  0.000    cross   0.000    along  0.000    timebias 0.0000

date 19980109 seconds   720    radial  0.000    cross   0.000    along  0.000    timebias 0.0000

date 19980109 seconds   960    radial  0.000    cross   0.000    along  0.000    timebias 0.0000

date 19980109 seconds  1200    radial  0.000    cross   0.000    along  0.000    timebias 0.0000

date 19980109 seconds  1440    radial  0.000    cross   0.000    along  0.000    timebias 0.0000

date 19980109 seconds  1680    radial  0.000    cross   0.000    along  0.000    timebias 0.0000

date 19980109 seconds  1920    radial  0.000    cross   0.000    along  0.000    timebias 0.0000

date 19980109 seconds  2160    radial  0.000    cross   0.000    along  0.000    timebias 0.0000

date 19980109 seconds  2400    radial  0.000    cross   0.000    along  0.000    timebias 0.0000

date 19980109 seconds  2640    radial  0.000    cross   0.000    along  0.000    timebias 0.0000

date 19980109 seconds  2880    radial  0.000    cross   0.000    along  0.000    timebias 0.0000

date 19980109 seconds  3120    radial  0.000    cross   0.000    along  0.000    timebias 0.0000

date 19980109 seconds  3360    radial  0.000    cross   0.000    along  0.000    timebias 0.0000

date 19980109 seconds  3600    radial  0.000    cross   0.000    along  0.000    timebias 0.0000

Note: For the Difference files, all radial track, cross track and along track differences are in units of meters.  The timebias unit is seconds.

## Appendix B	Generic Normal Point Software

### B.1	Introduction

The Generic Normal Point software was rewritten and upgraded to improve the data quality and fitting techniques used to more modern methods.  This report covers the benchmarking of the new version on the Alpha VMS computer.

### B.2	Benchmark Test Set

The test set consisted of passes taken at a variety of NASA SLR sites.  The satellites processed included most of the operational satellites.  The passes and stations are provided with the test results.

### B.3	Test Procedures

The verification of the software upgrade involved the comparison of the normal points formed by 1) the old VMS version of the normal point software – Merit II, 2) the new VMS version, 3) the field generated normal points, and 4) the full-rate data.  To perform this, the benchmark test set was determined and the full-rate data was processed by each of the four normal point generation packages.  An orbit fit was then performed using the full-rate data and the orbit determination software package GEODYN.  Once a stable orbit was generated, this orbit was then passed through each of the sets of Merit II normal point data.  The GEODYN summary, listing each data sources number of observations, the number of points that were within 3-sigma of the full-rate data fit, and the mean fit offset and the rms, was extracted and placed into a spreadsheet.  This spreadsheet was analyzed to verify the new software.

### B.4	Results

The final version of the Generic Normal Point software was found to determine the valid observations from noisy passes better than the present operational version.  Most of the passes mean offsets were within 2 millimeters.  The old version generated 13 observations that were not within 3 sigma of the full rate data, while the new version generated only 2, and generated more valid normal points than the current version.

### B.5	Conclusions

The present operational version written in 1986, based on the 3 satellites tracked by the network, has suited the network well. But, with the wide variety of satellites now tracked, this version performs the function better.  It is recommended that this version become the operational version.

## Appendix C 	GEODYN and Generic Normal Point Analysis Results

|  |  |  | GEODYN FULL RATE ANALYSIS | GENERIC NP GEODYN ANAL | NEW NP GEODYN ANAL | ONSITE NP GEODYN ANAL |
| --- | --- | --- | --- | --- | --- | --- |
| Filename | Sat id | Station | obs | Accept | Mean (m) | RMS (m) | PTS | Acc | Mean (m) | RMS (m) | PTS | Acc | Mean (m) | RMS (m) | PTS | Acc | Mean (m) | RMS (m) |
| LAGM40421A | LAGEOS | Mon Pk | 2874 | 2307 | 0 | 0.0112 | 18 | 17 | -0.0003 | 0.0023 | 18 | 18 | 0.0007 | 0.0056 | 19 | 18 | 0.0005 | 0.0052 |
| LAGM40518A | LAGEOS | Mon Pk | 537 | 498 | 0 | 0.0115 | 10 | 9 | 0.0002 | 0.0023 | 9 | 9 | -0.0001 | 0.002 | 10 | 9 | 0.0009 | 0.0029 |
| LAGM50411A | LAGEOS | YARG | 2296 | 2296 | 0.0051 | 0.0104 | 17 | 17 | 0.0059 | 0.0087 | 17 | 17 | 0.0059 | 0.0085 | 17 | 17 | 0.0072 | 0.0105 |
| 7105_980514_8001 | GFZ-1 | Mob-7 | 393 | 386 | 0 | 0.0089 | 31 | 30 | 0.0015 | 0.0049 | 31 | 31 | -0.0003 | 0.0039 | 31 | 31 | -0.002 | 0.0043 |
| 7105_980518_8001 | GFZ-1 | Mob-7 | 136 | 131 | 0.0008 | 0.0096 | 17 | 17 | -0.0004 | 0.0056 | 18 | 18 | 0.0005 | 0.0078 | 18 | 18 | 0.0017 | 0.0093 |
| 7105_980519_8001a | GFZ-1 | Mob-7 | 47 | 47 | 0.0004 | 0.0097 | 12 | 12 | -0.0004 | 0.0057 | 13 | 13 | -0.0001 | 0.0051 | 13 | 13 | -0.0011 | 0.0058 |
| 7105_980519_8001b | GFZ-1 | Mob-7 | 588 | 572 | -0.0001 | 0.009 | 35 | 35 | 0 | 0.003 | 35 | 35 | -0.0002 | 0.0029 | 35 | 35 | 0.0002 | 0.0034 |
| 7105_980601_8001 | GFZ-1 | Mob-7 | 83 | 58 | 0.0007 | 0.0108 | 4 | 4 | -0.0015 | 0.0038 | 4 | 4 | 0.0012 | 0.0039 | 4 | 4 | -0.008 | 0.0098 |
| 7105_980607_8001 | GFZ-1 | Mob-7 | 169 | 159 | -0.0002 | 0.0105 | 10 | 10 | 0.0011 | 0.0069 | 9 | 9 | -0.0002 | 0.0035 | 9 | 9 | -0.0045 | 0.0059 |
| S87Y98D223T2334_1500 | Ajisai | Mob-7 | 2318 | 2156 | 0 | 0.0126 | 22 | 22 | 0.0003 | 0.0025 | 22 | 22 | -0.0001 | 0.0025 | 22 | 22 | 0 | 0.0036 |
| s78y98d223t2315_1500 | Ajisai | HALL | 34 | 34 | 0.0041 | 0.0228 | 5 | 5 | 0.0047 | 0.0126 | 5 | 5 | 0.0042 | 0.0117 | 5 | 5 | 0.0048 | 0.0124 |
| S25Y98D224T0335_1500 | Ajisai | MLRS | 1087 | 788 | 0.0062 | 0.0178 | 11 | 11 | 0.0047 | 0.0078 | 12 | 12 | 0.007 | 0.0082 | 18 | 12 | 0.0059 | 0.007 |
| S84Y98D223T1721_1500 | Ajisai | Mon Pk | 133 | 103 | 0.0001 | 0.0152 | 4 | 3 | 0.0003 | 0.0011 | 4 | 4 | -0.0053 | 0.0103 | 4 | 3 | 0.0007 | 0.0015 |
| S64Y98D224T0353_1500 | Ajisai | T3 | 782 | 734 | 0.0002 | 0.0156 | 14 | 14 | -0.0043 | 0.0069 | 14 | 14 | -0.0039 | 0.0067 | 14 | 14 | -0.0029 | 0.0074 |
| s84y98d220t1503_4377 | Topex/Pos | Mon Pk | 1466 | 1275 | 0 | 0.0142 | 26 | 26 | 0.0005 | 0.0049 | 26 | 26 | -0.0002 | 0.0048 | 26 | 26 | 0.0001 | 0.0057 |
| s84y98d220t1304_4377 | Topex/Pos | Mon Pk | 2004 | 1795 | 0.0031 | 0.0259 | 47 | 47 | 0.0025 | 0.0251 | 47 | 47 | 0.0017 | 0.0251 | 47 | 47 | 0.0037 | 0.0232 |
| LA2M70421A | LAGEOS-2 | Mob-7 | 1406 | 873 | 0.0001 | 0.0123 | 14 | 14 | -0.0014 | 0.0053 | 14 | 14 | -0.002 | 0.0051 | 14 | 14 | -0.0021 | 0.0052 |
| LA2M70424A | LAGEOS-2 | Mob-7 | 324 | 253 | 0.0001 | 0.0107 | 7 | 6 | -0.0029 | 0.0083 | 10 | 10 | -0.0021 | 0.0055 | 10 | 8 | -0.0029 | 0.0074 |
| LA2M70425A | LAGEOS-2 | Mob-7 | 510 | 388 | 0 | 0.0106 | 6 | 5 | -0.0005 | 0.0018 | 5 | 5 | -0.0006 | 0.0018 | 7 | 5 | -0.0007 | 0.0022 |
| LA2M70411A | LAGEOS-2 | Mob-7 | 1153 | 387 | 0..0 | 0.0147 | 6 | 1 |  |  | 5 | 5 | -0.0011 | 0.0026 | 6 | 5 | 0.0009 | 0.0021 |
| LA2M70421B | LAGEOS-2 | Mob-7 | 121 | 88 | -0.0002 | 0.0097 | 3 | 2 | 0.0023 | 0.0034 | 1 | 1 | 0.0074 | 0 | 3 | 2 | 0.0022 | 0.0033 |
| S87Y98D224T0304_5986 | LAGEOS-2 | Mob-7 | 109 | 109 | 0 | 0.0088 | 3 | 3 | -0.0022 | 0.0046 | 3 | 3 | -0.0017 | 0.0036 | 3 | 3 | -0.0021 | 0.0046 |
| LA2M40517A | LAGEOS-2 | Mon Pk | 52 | 27 | 0.0037 | 0.0146 | 3 | 2 | 0.0014 | 0.0205 | 3 | 2 | 0.0003 | 0.0048 |  |  |  |  |
| s84y98d223t0409_5986 | LAGEOS-2 | Mon Pk | 4293 | 3305 | 0 | 0.0106 | 17 | 17 | 0.0005 | 0.0026 | 17 | 17 | 0.0005 | 0.0022 | 17 | 17 | 0.0005 | 0.0033 |
| LA2M50411A | LAGEOS-2 | YARG | 7057 | 7016 | 0 | 0.0082 | 27 | 27 | 0.0001 | 0.0014 | 27 | 27 | -0.0001 | 0.0014 | 27 | 27 | -0.0002 | 0.0019 |
| LA2M50417A | LAGEOS-2 | YARG | 5809 | 5776 | -0.0004 | 0.0083 | 21 | 21 | -0.0004 | 0.0025 | 21 | 21 | -0.0004 | 0.0026 | 18 | 18 | -0.0006 | 0.0013 |
| LA2M50418A | LAGEOS-2 | YARG | 10335 | 10294 | -0.0001 | 0.0083 | 29 | 29 | -0.0005 | 0.0013 | 29 | 29 | -0.0004 | 0.0014 | 27 | 27 | 0.0004 | 0.0032 |
| LA2M50418B | LAGEOS-2 | YARG | 9884 | 9827 | -0.0001 | 0.0084 | 28 | 28 | 0.0001 | 0.0011 | 28 | 28 | -0.0002 | 0.0013 | 26 | 26 | 0.0001 | 0.0024 |
| LA2M50426A | LAGEOS-2 | YARG | 1244 | 1236 | 0 | 0.0085 | 7 | 7 | -0.0008 | 0.0025 | 11 | 10 | 0.0028 | 0.0075 | 11 | 11 | -0.0007 | 0.005 |
| LA2M50428A | LAGEOS-2 | YARG | 3071 | 3012 | 0.0015 | 0.0103 | 19 | 19 | 0.0033 | 0.0058 | 19 | 19 | 0.0029 | 0.0049 | 19 | 19 | 0.0034 | 0.0062 |
| S78Y98D211T1024_3535 | GPS-35 | HALL | 31 | 29 | -0.0004 | 0.0207 | 8 | 8 | -0.0013 | 0.0118 | 8 | 8 | 0.0086 | 0.0247 | 9 | 9 | -0.0032 | 0.0124 |
| S78Y98D212T1054_3535 | GPS-35 | HALL | 64 | 61 | 0.001 | 0.0179 | 20 | 20 | -0.0014 | 0.0143 | 20 | 20 | -0.0009 | 0.0114 | 20 | 20 | -0.0011 | 0.0142 |
| s86y98d046_3535 | GPS-35 | mob-6 | 179 | 146 | 0 | 0.011 | 2 | 2 | -0.0012 | 0.0017 | 2 | 2 | -0.0014 | 0.002 | na | na |  |  |
| s86y98d118_3535 | GPS-35 | Mob-6 | 537 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | na | na | 0 | 0 |
| S84Y98D233T1128_3535 | GPS-35 | Mon Pk | 994 | 776 | 0 | 0.0179 | 5 | 5 | -0.0006 | 0.0016 | 5 | 5 | -0.0015 | 0.0022 | 5 | 5 | 0.0006 | 0.0021 |
| s84y98d220t0430_5050 | Meteor-2 Fiz | Mon Pk | 882 | 862 | 0.0002 | 0.0093 | 24 | 24 | -0.0009 | 0.0104 | 24 | 24 | -0.0009 | 0.0104 | 24 | 24 | -0.0022 | 0.0129 |
| S87Y98D224T0315_0643 | Stella | Mob-7 | 349 | 329 | -0.0022 | 0.0091 | 4 | 4 | -0.0027 | 0.0033 | 4 | 4 | -0.0028 | 0.0033 | 4 | 4 | 0.0014 | 0.0037 |
| S25Y98D224T0454_0643 | Stella | MLRS | 911 | 890 | 0 | 0.0117 | 10 | 10 | -0.0011 | 0.0028 | 10 | 10 | -0.0013 | 0.0026 | 10 | 10 | -0.001 | 0.0045 |
| S64Y98D224T0259_0643 | Stella | T3 | 532 | 460 | -0.0002 | 0.0103 | 13 | 13 | 0.0023 | 0.0079 | 13 | 13 | 0.0015 | 0.0082 | 13 | 12 | -0.0006 | 0.0035 |
| S85Y98D210T1056_3636 | GPS-36 | Yarg | 63 | 63 | 0.0007 | 0.0084 | 5 | 5 | 0.0007 | 0.0036 | 5 | 5 | 0.0006 | 0.0032 | 10 | 7 | -0.0074 | 0.0173 |
| S85Y98D216T1204_3636 | GPS-36 | Yarg | 218 | 134 | 0.0001 | 0.0147 | 0 | 0 | 0 | 0 | 2 | 2 | -0.0017 | 0.0046 | 2 | 2 | -0.0025 | 0.0036 |
| s87y98d224t0951_9071 | Glonass-71 | Mob-7 | 24 | 24 | 0.0043 | 0.0198 | 1 | 1 | 0.0046 | 0 | 1 | 1 | 0.0016 | 0 | 1 | 1 | 0.0043 | 0 |
| s87y98d224t0906_9071 | Glonass-71 | Mob-7 | 656 | 653 | 0.0221 | 0.0288 | 6 | 6 | 0.0207 | 0.0242 | 6 | 6 | 0.0207 | 0.0242 | 6 | 6 | 0.0205 | 0.024 |
| s25y98d224t0924_9071 | Glonass-71 | MLRS | 1803 | 17371 | -0.0073 | 0.0565 | 6 | 6 | -0.0064 | 0.0109 | 6 | 6 | -0.0096 | 0.0145 | na | na | 0 | 0 |
| s84y98d223t1014_9071 | Glonass-71 | Mon Pk | 1942 | 1833 | 0.0096 | 0.0297 | 5 | 5 | 0.0089 | 0.0111 | 5 | 5 | 0.0083 | 0.0102 | 5 | 5 | 0.0083 | 0.0105 |
| S84y98d223t1052_9071 | Glonass-71 | Mon Pk | 4425 | 4247 | 0 | 0.0332 | 8 | 8 | -0.0006 | 0.0022 | 8 | 8 | -0.0027 | 0.0036 | 8 | 8 | -0.0011 | 0.0024 |
| S87Y98D224T0327_6178 | ERS-2 | Mob-7 | 89 | 81 | -0.0002 | 0.0068 | 7 | 6 | -0.0006 | 0.0029 | 6 | 6 | -0.0009 | 0.0029 | 7 | 6 | 0.0046 | 0.0069 |
| S25Y98D224T0505_6178 | ERS-2 | MLRS | 675 | 642 | 0 | 0.0129 | 9 | 9 | 0.0007 | 0.0054 | 11 | 11 | -0.0014 | 0.0042 | 11 | 11 | 0.0021 | 0.0066 |
| S64Y98D224T0316_6178 | ERS-2 | T3 | 445 | 321 | 0.0028 | 0.0068 | 10 | 10 | 0.0033 | 0.0044 | 10 | 10 | 0.0042 | 0.0052 | 10 | 10 | 0.001 | 0.004 |